## Slide 1: Predicting MSYE
Multisite Yield Efficiency at Chip Testing

## Slide 2: MSYE – The challenge

## Slide 3: Semiconductor Final Test
Typical 16-site tester board with sockets
Simulation lot run
  16 sites
  75% yield
  150 touchdowns (150*16 = 2400 units)
Simulated Yield at each TD out to 1000TD
Simulated MSYE at each TD out to 1000TD
MSYE = Total Lot Yield / Yield of Highest Yielding Site. Can be measured at any TD on cumulative results.
Because
Test Lot material is from the same manufacturing lot
Test H/W is duplicate in each site
Performance should be the same in all test sites (Yield, Parametrics, etc)

## Slide 4: MSYE Example Product
Actual 1Q19 graph of MSYE for one product
Detection limit calculated based on simulation results
  Limit = 0.6 + 0.4 * ln(x)
Objective is to prevent excursions below the detection limit by predicting when a setup is drifting into that region
Simulation envelope
Detection limit

## Slide 5: Predicting MSYE
We are using variation in MSYE to detect equipment failures
Sometimes, there appears to be degrading performance, followed by fail
  In these cases, product and productivity are both lost until fail is detected and corrective action taken
Sometimes, fails seem to come out of nowhere
In both cases, there can be long periods of undetected “marginal” performance
Machine Learning Questions:
  Can we learn to predict the failures?
  Can we figure out which (of the many) variables are strongest impact to failures?
Degrade to fail
Marginal - Undetected

## Slide 6: Selecting a model

## Slide 7: The Basics
I want to predict MSYE
  This is a value – not categorization
  Need to use some type of Regression model
Here is the data
  That is a lot of input variables - and that is not even all of them
    Needs to be a Multple Regression of some type
  Note that some of them are Time – this matters later
Great – Which MR model?
  Much reading on the merits – Did not help me decide
  Finally, decided to just experiment with a bunch of models
    I would surely learn something
Setup Success DB

## Slide 8: Model Selection
Played with 10 or so
From Class
  LinearRegression
    R2 < 0.4
  Keras Neural Net Regressor
    Plain did not work, accuracy > 1%
Read some more sklearn documentation
  RidgeLinear
  BayesianRidgeLinear
  MLP_NeuralNet Regressor
  RandomForest Regressor
RandomForest has best R2 at 0.62
  But what are all those bad calls with actual of 1, but prediction as low as <0.7?
How do I choose?????

## Slide 9: Final Selection
Standard Deviation of RF is better
  BR outliers are spread more widely than RF
  BR inliers are very tight
It’s a puzzle
  Random Forest looks so good, but has a few really bad predictions
  Small lots!
    Remove
    Update the dataset
  RandomForest wins!!!!
    Final Y_test R2 = 69%
Outliers
Inliers

## Slide 10: Predicting the future

## Slide 11: Do Not Lose the Objective - Prediction
Back to the Books
  Need to predict what is going to happen – and be mostly right
  Read, Read, Read – I can’t make sense of this stuff!!
    Finally, just took some sample code (stock market predicting) and started adapting it step by step into my code
  OK, the trick is to shift the Y (output) training data
    ML then see the future outputs as the result of present inputs
      Voila! The future is predicted
Unfortunately
  R2 Score: -0.03734763664152818

## Slide 12: Think About Prediction Again
My teaching example
  Stock market
  One stock (GOOG)
My data
  An entire month of data from a factory
  Many products, many testers
  Not in sequence
Oops – Shifting out of sequence data is just dumb!
Gotta do this again – with appropriately sequential data

## Slide 13: Identifying impactful variables

## Slide 14: Impactful Variables
Need to start with Principal Component Analysis
  Did one round with Chris’s help
  Results did not seem to make sense
  Could not quickly translate back to features to try to understand
Random Forest Regression
  Result provided is feature_importance
  Not sure I understand what this is
    Certainly not the same as LinearRegression coefficients
    Great! More studying. Read, Read, Read
Basically never got a good start on evaluting variable impact

## Slide 15: Current status

## Slide 16: Current Status
Started with two questions
  Can we learn to predict the failures?
  Can we figure out which (of the many) variables are strongest impact to failures?
Predicting failures
  Proved out a ML model with R2 @ 0.69
    Model was against 1 month, 1 factory data
      372 Test Cells, 895 Products, 13,413 Lots
    Considering all the variables – pretty good
  Additional work required for time predictions
    The Y-shift must be rotated by Test Cell and probably by Product or Product Family
    But I am optimistic
Identifying impactful variables
  Did not really get started

## Slide 17: What is Next
Figure out how to be time predictive
Analyze Feature Importance
Once all this is working with Random Forest Regression, go back and try some other models again
Try on data from other factories
Then there is an entire journey of convincing people this is useful, figuring out how to deploy and use to improve cost and productivity